## Slide 1: The Complete Guide to Mounting Images

## Slide 2
Cutting mounts for images doesn’t have to be a complicated process, and hopefully this presentation will outline a few of the subtleties toward achieving better outcomes.
Having the knowledge is one thing, but having the right tools for the project can often be the difference between success and failure.
The tools used in this presentation are from local company “Frameco” and were developed specifically towards the DIY market giving the ability to achieve professional results.

## Slide 3: The Critical first steps
There are a couple of key factors to go through before we start cutting that will influence the end result.
Mat colour
Mat Size
Style

## Slide 4: Mat Colour
Choosing the right mat colour is crucial to the end result – the wrong selection will distract the viewer away from the image rather that draw them in.
Primary mat colour should have a connection with one of the key points in your image
Double mats are a great way to introduce the “connection” colour which can often be too dominating on its own.

## Slide 5: Make Mat size and colour work for you
A single mat that supports the overall image.
A double mat that introduces a “complimentary” colour and draws the viewer in.

## Slide 6: Mat Size
The actual size of the mat boarder plays a far greater role than many people think.
The wider the boarder the more the viewer is drawn into the image.
Mat Boarders should never be less than 65cm – at that sizing you can cut 6 mats from one full sheet - 3 for an 8 x12 image and 3 for an 8 x 10

## Slide 7: Style
There are several different styles of mat cutting that will add extra impact to your images. Once you grasp the concept of cutting a single mat you can easily achieve any of the styles outlined

## Slide 8: Single Mount There are a couple of different things you do with a single mat that can increase its impact without introducing extra mats.
A bottom heavy mat which works very well with perspective images
Add a “v” Grove line which give the illusion of being a double mat.

## Slide 9: Double Mount
Adds extra interest
Can make image appear sharper
Draw the viewer in.

## Slide 10: Triple Mount
Same as a double only on a far greater scale.
There are several options you can use.
Can create a 3D effect.

## Slide 11: Now we’re ready to start!!

## Slide 12: Measuring your image
The first step to determine the overall size of our mat board is to measure the image.
Measure the length and width of the image you wish to mount, then subtract 5mm from each measurement.
Example – 355x265 becomes 350 x260. this is to allow some image to sit behind the opening.
355cm
265cm

## Slide 13: Determining our mat size
Take our previous image measurement and working on a boarder of 70 mm add them all together.
Example
Width = 70+70+350 = 495mm
Height = 70+70+260 = 400mm
Which means our overall mat size will be 400x495 mm
Height =70+70+260=400mm
Width = 70+70+350=495mm

## Slide 14: Marking out your mat
With your mat board cut size (495x400) now it’s time to mark it out for cutting.
Lay your mat face down on a sheet of grey box board (don’t use self healing mats as they are too dense and will break you blades)
Measure in from the edge 70mm and draw a line all the way through. Continue this until you end up with the same as pictured here.

## Slide 15: Cutting your Mat
Before you start cutting place your image on your mat to ensure there is plenty of overlap.
With your mat face down on your grey box board place your Mat Master ruler on your mat so your line is just visible.

## Slide 16: Cutting your Mat
Next place your mat cutter on the ruler channel and align the white start/stop mark just behind your bottom pencil line.
Before you start drop your arm, so you are pushing behind rather than down on the cutter this will help eliminate overcuts.
Press the blade into the board and push the cutter away from you towards the finish pencil line. Release the handle and the blade will retract
Rotate the mount clockwise by 90 degrees and repeat for the remaining sides. Turn your mat over to reveal your bevel mount.

## Slide 17: Mounting Your Image
Place your new mount onto a piece of foam core board and cut around it to create a backing board the same size as your mat.
With your mat board on top of the backing board and aligned on all edges carefully and lightly mark the top 2 corners of the mount opening onto the backing board.
Remove your mat board and with a ruler and pencil extend the lines to the outside of the backing board.
There are a couple of different ways to mount images but today we will concentrate on the “Basic Method”.
Materials required are:
3mm foam core
Mounting tape
Double sided tape
Pencil
Trimming Knife
Ruler

## Slide 18: Mounting Your Image (continued)
Now position your image over those pencil marks as shown here.
Carefully place your mat over the top again to check image alignment to the mat opening. When satisfied remove the mat and fasten with 2 pieces of mounting tape as shown by yellow arrows.
Note: Never place tape top and bottom of image to allow to “move”
Now run double sided tape along the edges of the backing board as shown in red. Peel back about 40 mm of paper on each row of tape to make placement of mat easier.
Place your mat board back on top and align all edges. When satisfied slowly remove one row of tape paper and press down on that edge. Now slowly remove all the other tape paper but don’t press down until all is removed.
FINISHED!
Double sided tape
Peel back
paper